## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
ECE 382V: QUANTUM COMPUTING SYSTEMS:
A SOFTWARE/ ARCHITECTURE PERSPECTIVE
BANDWIDTH Problem
IN QEC

## Slide 2
Cryogenic Control Processors For Large Scale Quantum
Cryogenic control processors operate at 4K inside dilution refrigerator (closer to the qubits)
Control Processor
Qubits
20mK
300K
(27oC)
Metal Wires
 Thermal Leakage
Qubits
20mK
Control Processor
Superconducting wires
 Low Leakage
4K
(-269o C)
Intel Horse-Ridge
Google Cyro-CMOS
Superconducting
https://www.intel.com/content/www/us/en/newsroom/news/2nd-gen-horse-ridge-cryogenic-quantum-control-chip.html
https://blog.research.google/2019/02/on-path-to-cryogenic-control-of-quantum.html

## Slide 3
Cryo-CMOS vs. Superconducting Devices at 4 Kelvin
Currently, research efforts in both directions
Cryo-CMOS
Superconducting
Josephson junction as a switch
2 picosecond switching time (even faster)
Low device densities
Lack of dense memories
Unique challenges that limit usage of current EDA tools, harder to fabricate
Ultra-low power dissipation
Transistor as a switch
Faster switching at cryo temp. than room
Large device densities
Dense memory solutions
Relatively easy to fabricate after several years of development in EDA toolchains
Large power dissipation
Large cooling overheads (1000x), limited power budgets (1W or below)

## Slide 4
CONTROL BANDWIDTH
Manage QEC in hardware, share QEC instructions to improve scalable architectures

## Slide 5
Control Processor Supplies QEC Instructions
Instruction supply must be deterministic and timely
Qubits
Control Processor
Uncorrectable Errors !!

## Slide 6
Instruction Bandwidth Bottleneck
Instruction bandwidth bottleneck is a problem, 99.99% of instructions are for QEC
Can’t use
i-cache
Delay in delivery of QECC instructions causes errors to accumulate [cannot use software managed QEC and caches]
Required instruction bandwidth scales linear in number of qubits
Shor’s Algorithm
Instruction Bandwidth (B/s)
Total Bandwidth
Non-QECC Bandwidth
Number of Qubits
QECC Bandwidth Bloat – 10,000X
128 bit
256 bit
1024 bit

## Slide 7
QEC Instruction Overheads
QEC instruction bloat is dominant in all large scale quantum workloads

## Slide 8
Manage QEC Using Micro-Code
Issue micro-ops locally, managed fully in hardware
Micro-Code Engine (MCE) continuously issues QECC µops from local µcode
Master controller issues regular instructions. MCE decodes it to µops
Master Controller
Control Processor
µ-Code
Engine
µ-Code
Engine
µ-Code
Engine
µ-Code
Engine
Qubits
Swamit Tannu et al. “Taming the Instruction Bandwidth of Quantum Computers via Hardware Managed Error Correction”, MICRO 2018

## Slide 9
Micro-Code Engine Based Architecture
Leverage multiple thermal domains for improved efficiency

## Slide 10
Managing Logical Operations And QEC Operations
Dedicated QEC microcode is continuously run to manage QEC, logical microcode is interspersed
QECC Microcode  supplies QECC µops to all qubits
Logical Microcode  supplies logical µops
Mask Bits  selects between QECC µop and Logical µops
Quantum Execution Unit

## Slide 11
Micro-Code Memory Scaling
Microcode memory capacity requirement increase linearly in the number of qubits
µ-Code
C bits
Log(N) bits
QECC µops
Qubits

## Slide 12
Superconducting Memory Capacity Limits #Qubits
4Kb µcode memory can only support about 35 qubits
Capacity of state of the art JJ based Memory

## Slide 13
QEC Instructions Have Spatial Locality
QECC instruction patterns are leveraged to minimize µcode capacity
QECC have spatially repeating instruction blocks -- Unit Cell
Unit-Cell µops can generate QECC µops for all the qubits
A
B
C
D
A
B
C
D
A
B
C
D
Qubit1
Qubit12
Unit Cell
QECC
µops
A
B
C
D
Unit Cell

## Slide 14
Microcode Sharing Via Unit Cell Improves Scalability
Microcode can service up to 2000 qubits with 4Kb of microcode
Capacity of state of the art JJ based Memory
O(1)
RAM
FIFO
UNIT
CELL
UNIT
CELL
For 4Kb Memory Budget
90x

## Slide 15
Syndrome BanDWIDTH
Transmit compressed syndromes, enable multi-level decoding

## Slide 16
Syndrome Transmission Bandwidth Requirement
Syndrome transmission requires 100-1000s of Gigabits per sec bandwidth

## Slide 17
Syndrome Compression
Compressing syndromes enable us to send more data per unit time
Each error flips two parity qubits
Long error-chains have fewer parity flips
3d3 fault locations
  6d3p possible non-zero syndrome bits
d = 11, p = 10-3
  8 non-zero bits in 1000-bit syndrome
Insight: Syndrome data is sparse, can be compressed

## Slide 18
Dynamic Zero Compression
Data compression is well-studied in conventional systems, work well for syndrome compression
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Zero Indicator Bit Vector
0
0
0
0
0
0
0
0
0
1
0
0
Transmit
0
0
0
0
0
1
Zero Indicator Bit Vector
Transmit
0
0
1
0
1
0
0
Dynamic Zero Compression for Cache Energy Reduction, Luis Villa, Michael Zhang, and Krste Asanovic, MICRO 2000

## Slide 19
Sparse Representation
Compression ratio depends on error rates with average reduction of 30x. Typically sparse representation outperforms for larger distances and low physical error-rates
0
0
0
0
0
0
0
0
0
0
0
0
1
Sparse Representation Bit
0
0
0
0
0
0
0
0
0
1
0
0
Transmit
1
0
Sparse Representation Bit
Transmit
0
1
0
0
1
Sending the indices of non-zero syndrome bits
Fast compression/de-compression using low logic density

## Slide 20
Hierarchical Decoding
Key Idea: Only send complex error events to a complex decoder, decode others locally
Nicolas Delfosse, Hierarchical decoding to reduce hardware requirements for quantum computing

## Slide 21
System-Level View: Decoding Outside Refrigerator
Bandwidth bottleneck: could require up to Tbps for certain applications
COMPLEX
COMPLEX
COMPLEX
COMPLEX
COMPLEX
300 K
L
B
4 K
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
Low latency needed for functional correctness!!
1 microsecond
1000 L * 1000 P = O(1,000,000) qubits
300 K
4 K
Metal Interconnects
Superconducting Wires
H B
20 mK
20 mK
1
2
3
4
5
E: Error Signatures

## Slide 22
System-Level View: Decoding Inside Refrigerator
Cryo-power bottleneck: Limited cryogenic power budget (~1W)
4 K
COMPLEX
COMPLEX
COMPLEX
COMPLEX
COMPLEX
L
B
E
E
E
E
E
E
E
E
E
E
E
E
E
E
E
1000 L * 1000 P = O(1,000,000) qubits
300 K
P = 1W
300 K
4 K
Metal Interconnects
Superconducting Wires
P = ~1W
H B
20 mK
20 mK
1
2
3
4
5
E: Error Signatures

## Slide 23
Not All Error Events Are Equally Hard To Decode
Separately decode trivial (inside refrigerator) and complex (outside refrigerator) error events
E
E
E
E
E
E
E
E
E
E
T
T
T
C
T
T
C
T
T
T
Easy to separate!
Most errors are trivial!
T: Trivial-to-decode
C: Complex-to-decode

## Slide 24
Isolated Error Events Vs. Error Chains
Most error events are isolated and trivial to decode, send them to small decoder (Clique)
C
(<1 - 10 %)
1
T
(90 - 99+ %)
1
Error chains: Hard to decode and relatively rarer!!
T: Trivial-to-decode
C: Complex-to-decode
Isolated errors: Trivial to decode and very common!!

## Slide 25
System-Level Overview In Presence Of Clique Decoder
Reduces bandwidth requirement by decoding trivial syndromes locally. Reduces hardware requirement by decoding complex syndromes off-chip outside refrigerator.
T
T
T
T
T
T
T
T
T
T
T
T
T
T
T
1
2
3
4
5
CLIQUE
CLIQUE
CLIQUE
CLIQUE
CLIQUE
C
C
C
C
COMPLEX
COMPLEX
COMPLEX
COMPLEX
COMPLEX
4 K
300 K
H
B 20 mK
L
B
300 K
4 K
20 mK
Metal Interconnects
Superconducting Wires
BW
reduction
HW
reduction
Gokul Ravi et al., “Clique: Better Than Worst-Case Decoding for Quantum Error Correction”, ASPLOS 2023

## Slide 26
When Are Error Events Hard To Decode?
Chained errors trigger non-local syndromes that are more challenging to pair and decode
2
d
c b
a
1
1
{ 1
2 } :
X 9
X 4
a
b
c
2
d
Minimum Weight Perfect Matching
COMPLEX DECODER

## Slide 27
When Are Error Events Trivial To Decode?
Isolated errors only trigger locally paired syndromes which are easy to decode
2
a
1
4
b
3
2
a
1
4
b
3
CU
Unit of the Clique decoder
CLIQUE DECODER
CU
CU
CU
CU
CU
CU
CU
CU
CU
Code distance (d)
d
CU: ~10 combinational gates. Clique decoder: d2 CUs.
Linear Clique scaling wrt. physical qubits.

## Slide 28
Understanding Benefits Of Clique
The Clique decoder leads to significant reduction in bandwidth and cryogenic compute resources
85%
90%
95%
Errors decoded by Clique (%)
80%
5.00E-03 5.00E-04 5.00E-05
Qubit physical error rate
90 - 100% of decodes handled trivially by Clique, largely eliminating outside-fridge decoding.
Clique Coverage (d=15)
100%
1
10
100
1000
10000
5E-5/1E-15
Number of logical qubits
5E-3/1E-5 5E-4/1E-10
Physical ER / Logical ER
2.5M physical qubits!
Logical qubits (1W)
Clique supports 2.5M physical qubits at 1W power  1000s of logical qubits.
>90 % error events handled by Clique decoder leading to significant bandwidth savings

## Slide 29
Summary
Micro-code And Resource Sharing
QEC requires large bandwidth
Instruction BW reduced using ucode and resource sharing
Syndrome BW reduced by sending compressed syndromes
Syndrome BW reduced by using hierarchical decoding (+ resource savings)