## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
ECE 382V: QUANTUM COMPUTING SYSTEMS:
A SOFTWARE/ ARCHITECTURE PERSPECTIVE
ERRORS And BENCHMARKING
Thanks to Prof. Moinuddin Qureshi & Prof. Swamit Tannu!

## Slide 2
Decoherence: Qubits Lose Information Over Time
Higher coherence times are desirable, depends on qubit technologies
Time = 0
Time = t
1
0
1
0
Error
Decoherence: Qubit loses its information naturally due to its unwarranted interactions with the environment
Probability of decoherence increases exponentially with time
Probability of Qubit
in the Correct State
Time
Time Constant: Coherence Time
Phase information decays faster than amplitude information, therefore there are two different time constants (T1 for amplitude and T2 for phase, usually T2<T1)

## Slide 3
Quantum Gate Operations Are Imperfect
Lower gate error rates are desirable
1
0
Error
1
0
Quantum Gate
Quantum gate operations cannot be applied with precise accuracy
Error-rates typically in the range of 0.1-1 %
Error-rates of two-qubit gates are an order of magnitude higher than single qubit gates

## Slide 4
1
0
Quantum Measurements Are Error-Prone
Lower measurement errors are desirable
1
0
Error
1
0
Quantum Measurement
50%
50%
30%
70%
Quantum measurements produce incorrect ‘classical’ outcomes
State more prone to errors than state
Error-rates typically in the range of 1-4 %

## Slide 5
What Causes Hardware Errors?
Some noise sources are not yet completely understood, hard to fully eliminate at device-level
Let us take the example of a measurement operation on a superconducting qubit
Measure
0
1
Resonator
Amplifier
SNR+
Discriminator
0
1
300 K
20 mK
3-4 K
Frequency shift is sensitive to noise
Thermal noise
ADC
Long latency
Inaccurate classification
Software
Hardware

## Slide 6
Analyzing The Impact Of Hardware Errors
High error-rates of quantum hardware limits us from running most practical quantum algorithms
M
q0
q1
M
X
+
Let denote the probability of successfully executing operation on qubit
Let e denote the probability of error while executing operation on qubit
Let denote the probability of successfully running the entire circuit
0.1%
1%
3%
More accurate modeling by accounting for decoherence using exponential decay

## Slide 7
Qubit Device Level Metrics
What are the challenges if we want to compare qubits on two different machines?
Gate Fidelities (single-qubit, two-qubit, reset)
Coherence times
Measurement Fidelities (states 0 and 1)
Crosstalk metrics (operations on one qubit affect operations on other qubits, challenge for concurrent operations during a program)
Gate latencies (determines length of a program and the probability of decoherence)
Spectator errors (operations on one qubit affects the state of an idle/spectator qubit
Not all qubits are created equal: Temporal And spatial variation In error-rates

## Slide 8
Different Qubit Device Technologies
What are the challenges if we want to compare qubits on two different machines using same qubit technology?

## Slide 9
Different Systems Using Same Qubit Technology
Benchmarking metrics for qubits are different from those used for quantum computers
Might be using completely different basis gates
Different ways of building the same qubit
IBM
Google

## Slide 10
Circuit Reliability/Fidelity Metrics
Compile
Run
Log
Outcome
M
q0
q1
M
X
+
01
00
11
11
Program
Quantum
Device
Repeat N trials
11
Quantum
Executable
How to compute PST of a Bell-Pair circuit (multiple correct answers or output is a distribution)?

## Slide 11
Distance-Based Metrics
In order to compute PST or HD, the ideal output must be known
Outcomes
a
b
Prob.
0
1
Outcomes
a
b
Prob.
0
1
Outcomes
a
b
Prob.
0
1
D1
D2
D3
HD=0
HD=1
Bounded between 0 and 1
Total variational distance is also used

## Slide 12
Entropy
Entropy can be used to infer the amount of noise in a distribution
Let be the probability of sampling
Entropy is a measure of randomness (noise) in a system

## Slide 13
Why And How To Compare Two Quantum Computers?
There are many caveats in benchmarking
Enables us to compare the performance of the software
Quantify and compare the effectiveness of one quantum hardware over another
Benchmarking is common even in classical systems
Set technology milestones and track progress

## Slide 14
Analogy
Classical-> execution time, Quantum-> reliability/ application fidelity
Most suitable hardware for a given application
Best Hardware for on an average*

## Slide 15
Quantum Volume [Introduced by IBM]
How to design quantum volume circuits?
We need a metric that will capture – Number of qubits, gate fidelity, coherence time, connectivity, cross-talk, spectator errors ..
We want benchmarking circuits to be parametrizable as opposed to be fixed
IBM Quantum Volume satisfy above two properties

## Slide 16
Quantum Volume [Introduced by IBM]
Higher Quantum Volume (QV) is better
Generate randomized circuits that produce output distribution (P)
In P, the heavy strings are output strings with higher than median probability of occurrence
Start with “x” qubits and “x” circuit depth, generate large number of random circuits
Run each circuit on simulator get list of heavy strings, then run on real machine, if real machine can produce 2/3 of the heavy strings then it’s a success
Try the same for “x+1”
Quantum volume = 2x

## Slide 17
Quantum Volume Of IBM Hardware
What is the drawback of this approach?

## Slide 18
Benchmarking vs. Randomized Benchmarking (RB)
Randomized benchmarking corresponds to a finer granularity (and not full system)
“Benchmarking” is used in general-purpose computing to compare the performance of two different designs or impact of individual optimizations
Design-1: Given core model
Design-2: You enhance given core w/ security features
Which is better?
Are your enhancements causing slowdown?
“Randomized Benchmarking” is a protocol for characterizing the error-rates of different qubit devices and quantum operations (typically: granularity of single-qubit or two-qubit gates)

## Slide 19
Quantum System Calibration Using RB
The complexity of calibration scales with the system size
Calibration of a quantum processor includes state and gate fidelity estimation, optimization of on-chip component parameters (such as qubit frequencies, coupler, and readout resonator frequencies), and finding the optimal control parameters for high-fidelity quantum gates
Randomized benchmarking enables us to estimate the error-rates
Identity
How many times did we get the correct state?
Repeated execution
qubit
Randomized benchmarking may be of different types (simple, interleaved)
Notes: Check out: https://www.youtube.com/watch?v=fk2HH9M4FqA
To learn more on calibration

## Slide 20
SYSTEM CALIBRATION
CHALLENGEs
Thanks to Paul Klimov for sharing information about Google quantum systems!

## Slide 21
Xmon-Transmon Qubits
Quantum gates are performed by applying pulses operating at dedicated frequencies
Frequency Tunability
|1〉
~ 5 - 7 GHz
|0〉
Self Cap.
Xmon Qubit Circuit
XY line Resonator
9 Qubit Processor
(2013)
SQUID
Z line
Resonator for readout
XY line for microwave control
SQUID Z line for frequency control
Operate qubits from ~5 - 7 GHz
Notes: Check out: https://www.youtube.com/watch?v=fk2HH9M4FqA
To learn more on calibration

## Slide 22
Single Qubit Gates On Xmon Qubits
What about two-qubit gates?
idle frequency
R. Barends, J. Kelly, et al Nature 508, 500 (2014)
Single Qubit Gate:
Microwave Pulse
Single-qubit gates:
Microwave at idle frequency
|0〉
|1〉
Notes: Check out: https://www.youtube.com/watch?v=fk2HH9M4FqA
To learn more on calibration

## Slide 23
Two-Qubit Gates On Xmon Qubits
The gate frequency impacts the qubit qualities
R. Barends, J. Kelly, et al Nature 508, 500 (2014)
Two-qubit gates:
DC pulse to interaction frequency
interaction
frequency
Two-Qubit gate:
DC Current Pulses
Fixed Coupling*
|0〉
|1〉
|0〉
|1〉
Notes: Check out: https://www.youtube.com/watch?v=fk2HH9M4FqA
To learn more on calibration

## Slide 24
Impact Of Frequency Selection On Qubit Qualities
The qubit frequencies must be carefully chosen
T1 and T2 show complex frequency dependence
Fluctuations by >10x over >10 MHz
Mainly originates from two-level system (TLS) defects which are still a mystery (dielectrics? Quasiparticles?)
Energy-Relaxation
 |  | 200 MHz
 |  | 10-100x
Dephasing
0 T1 (μs) 50
0 T2 (μs) 100
 |  | 200 MHz
 |  | 10x
5.4
Frequency (GHz)
6.4
5.4
Frequency (GHz)
6.4
Notes: Check out: https://www.youtube.com/watch?v=fk2HH9M4FqA
To learn more on calibration

## Slide 25
Constraints For Frequency Selection
Frequency calibration is non-trivial
To enable high fidelities, idle and interaction frequencies
  Must avoid TLS during idles
  Must avoid TLS during interactions
  Must detune neighbor qubits during interactions
  And many more…
0 T1 (μs) 50
5.4
Frequency (GHz)
6.4
idle
idle
0 T1 (μs) 50 0 T1 (μs) 50
idle
idle
interaction
5.4
Frequency (GHz)
6.4
0 T1 (μs) 50 0 T1 (μs) 50
idle
idle
interaction
5.4
Frequency (GHz)
6.4
0 T1 (μs) 50 0 T1 (μs) 50
idle
interaction
5.4
Frequency (GHz)
6.4
Notes: Check out: https://www.youtube.com/watch?v=fk2HH9M4FqA
To learn more on calibration

## Slide 26
The Frequency Allocation Problem
Freq. allocation is a high-dimensional, high-constraint, non-convex,time-dependent optimization
Complexity
  N idle frequencies
  ~2N interaction frequencies
  For 100 qubits, ~1003N options
Processor
idle
interaction
Processor
idle
parasitics
Processor
parasitics interaction
Objective
  Respect control hardware specs
  Avoid TLS defects near idles, over interactions
  Avoid parasitic coupling b/w nearby qubits
~50/idle
~100/interaction

## Slide 27
Snake Optimizer: Overview
Accurate and fast calibration at scale is an open problem
Paul Klimov, “The Snake Optimizer for Learning Quantum Processor Control Parameters”
When do you calibrate?
Managing system downtimes?
Managing drifts and recalibrations?

## Slide 28
Summary
Error
Device level metrics
System-level metrics
Program-level metrics
System Calibration
Benchmarking/ Randomized Benchmarking