## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
ECE 382V: QUANTUM COMPUTING SYSTEMS:
A SOFTWARE/ ARCHITECTURE PERSPECTIVE
Measurement error MITIGATION

## Slide 2
Recap: Quantum Measurements Are Erroneous
Lower measurement (or readout) errors are desirable
1
0
1
0
Error
1
0
Quantum Measurement
50%
50%
30%
70%
Quantum measurements produce incorrect ‘classical’ outcomes
State is more to errors than state
Error-rates typically in the range of 1-4 %

## Slide 3
Why Are Measurements Error-Prone?
Example of a measurement operation on a superconducting qubit
Measure
0
1
Resonator
Amplifier
SNR+
Discriminator
0
1
300 K
20 mK
3-4 K
Frequency shift is sensitive to noise
Thermal noise
ADC
Long latency
Inaccurate classification
Software
Hardware

## Slide 4
Measurement Error-Rates Really High
We obtain an incorrect outcome even if one of the measurement operations fail
Chart: Worst-case Readout Error Rate
| ibmq_belem (16) | ibmq_quito (16) | ibmq_manila (32) | ibm_nairobi (32) | ibm_oslo (32) | ibm_algiers (128)
Error Rate | 2.72 | 7.2 | 3.5 | 10.93 | 14.44 | 25.05
Quantum Volume

## Slide 5
Simultaneous Measurements More Vulnerable
Measurement crosstalk increases with program size
Crosstalk
Isolated
Multiple
Chart: MEasureMENT Error Rates on GooglE SYCAMORE
| ISOLATED | MULTIPLE
Average | 6.14 | 7.73
Worst-Case | 11.7 | 20.9

## Slide 6
How To Reduce Measurement Errors?
We will cover some of these measurement error mitigation schemes
Device-level techniques for reducing measurement errors
Can we transform the circuit such that we measure most of the time?
Measurement errors are relatively easier to correct using post-processing
q0
q1
X
X
M
M
q0
q1
X
X
M
M
X
X
How do we know what is the output state of a program?
2%
q0
M
Outcomes
0
1
Prob.
q0
X
M
4%
Outcomes
0
1
Prob.
It incurs huge overheads (quantum + classical)
More accurate state classification

## Slide 7
Approach of STATE Transformation
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 8
Measurement Errors Have Bias
Goal: Flip and measure qubits in a less vulnerable state
22%
78%
Probability
ibmqx4
0
1
2
4
3
Measure
16%
84%
Probability
0
0
0
0
0
Correct Answer
All zero state
Measure
38%
62%
Probability
1
1
1
1
1
All one state
Measure
1
1
1
1
1
Invert
All one state

## Slide 9
Challenge: To Invert Or Not To Invert?
Flipping and measuring must be done with caution because we do not know the correct output
Measure
1
1
1
1
1
22%
78%
Probability
Invert
Measure
38%
62%
Probability
1
1
1
1
1
Correct Answer
Measure
0
0
0
0
0
42%
58%
Probability
Invert

## Slide 10
Measurement Error Mitigation Via State Transformation
More on generalization and bias estimation for efficient inversion in the paper
Measure
Invert
Measure
trials
trials
trials
Swamit Tannu et al. “Mitigating Measurement Errors in Quantum Computers by Exploiting State-Dependent Bias”, MICRO 2019

## Slide 11
Characterization + POST-Processing
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 12
Modeling Measurement Errors
How do we determine the probability ‘p’? How many Xs? How many Ys?
n-bit
Program
n-bit string
outcome
N= 2n possible
outcomes
Model measurement error as an operator that maps an n-bit outcome (say X) into another n-bit outcome (say Y) with some probability ‘p’
Example:
M
q0
q1
M
X
+
Produces 01 instead of 11
We can correct the measurement error using classical post-processing by re-mapping the incorrect n-bit outcome (Y) into the correct n-bit outcome (X) using probability ‘p’

## Slide 13
How Many Correct <-> Incorrect Mappings?
How do we best represent this?
N= 2n possible
outcomes
An outcome or bitstring maps to itself when there is no measurement error
An outcome maps to any one of the remaining (N-1) outcomes if measurement error occurs
The sum of probabilities of mapping to itself and mapping to all other outcomes must be 1
…

## Slide 14
Formulation Of A Noise Matrix
How can we prepare the noise matrix?
2n x 2n matrix
Row index corresponds to expected outcome/state
Column index corresponds to outcome/state after measurement
Entry[row][col] -> probability of obtaining the outcome corresponding to col if the expected outcome corresponds to row
2n
2n
00
01
10
11
00
01
10
11
Probability that state 11 is incorrectly measured as 00
Probability that state 00 is correctly measured as 00
Noise Matrix (M)
Example:

## Slide 15
The Inverse Noise Matrix
Multiplying with the inverse noise matrix rectifies the output distribution
N= 2n possible
outcomes
…
N= 2n possible
outcomes
…
When do we observe a certain state after measurement?

## Slide 16
How Do We Prepare The Noise Matrix?
Characterizing all possible basis states enables us to compute the noise matrix
Prepare an initial state (say |00⟩ state)
Repeat state preparation and measurement for a few thousand trials
Measure the qubits
Obtain probability distribution which corresponds to the row for the initial state
00
01
10
11
00
01
10
11
q0
q1
M
M
q0
q1
X
M
M
q0
q1
X
M
M
q0
q1
X
X
M
M
Repeat for other states (|01⟩ , |10⟩ , |11⟩)

## Slide 17
Matrix-Based Measurement Error Mitigation
What are the drawbacks of this technique (complete measurement error mitigation)?
Noise Matrix
Characterize
Inverse Noise Matrix
n-bit
Program
Post-process
Run Program
Noisy distribution
Measurement error-mitigated distribution

## Slide 18
Matrix-Based Measurement Error Mitigation Drawbacks
How do we reduce these overheads?
Noise Matrix
Characterize
Inverse Noise Matrix
n-bit
Program
Post-process
Run Program
Noisy distribution
Measurement error-mitigated distribution
Who characterizes?
How frequently?
Number of circuits?
Classical overheads?

## Slide 19
Reducing Complexity Of Matrix-Based Error Mitigation
This approach is known as tensored error mitigation. What are the drawbacks?
Overheads result from running an exponentially large number of characterization circuits and using an exponentially large inverse noise matrix
n-bit
Program
2n
possible states
…
n qubits
n-bit
Program
M x 2k
possible states
…
n qubits
M groups of k qubits
If n = 10, 1024 circuits, 1024 x 1024 matrix
If n = 10, k = 2,
5 x 4 = 20 circuits,
5 of 4 x 4 matrices
Complete or Global Correlation
Localized Correlation

## Slide 20
Selective Global Characterization
This approach captures correlated measurement errors while reducing complexity
Tensored error mitigation trades-off accuracy (does not capture correlation in measurement errors between qubit groups) for reduced complexity
n-bit
Program
Post-process
Run Program
Noisy distribution
Measurement error-mitigated distribution
Noise Matrix
Characterize
Inverse Noise Matrix
Characterize only the basis states observed in noisy distribution

## Slide 21
Example Of Selective Global Characterization
What are the drawbacks of this technique?
Program output distribution
Global Noise Matrix
Reduced Matrix
https://arxiv.org/pdf/2108.12518.pdf

## Slide 22
FEWER Measurements + Recompilation
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 23
Fewer Measurement Reduce Readout Crosstalk
Are high-fidelity circuits with partial measurements alone sufficient?
Measure fewer qubits and Reconstruct Distribution
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0 | 0 | 0 | 1
Chart: Outcomes (q0)
| 0 | 1
 | 0 | 1
Chart: Outcomes (q1)
| 0 | 1
 | 0 | 1
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0 | 0 | 0 | 1
X
Ideal

## Slide 24
Need For Correlation
Ideally, we want both correlation and high fidelity
X
Ideal
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0.5 | 0 | 0 | 0.5
Chart: Outcomes (q1)
| 0 | 1
 | 0.5 | 0.5
Chart: Outcomes (q0)
| 0 | 1
 | 0.5 | 0.5
Chart: Outcomes (q1q0)
| 00 | 01 | 10 | 11
 | 0.25 | 0.25 | 0.25 | 0.25
Correlation?

## Slide 25
JigSaw
JigSaw provides both correlation and high fidelity
. . .
Original program
Circuits with Partial Measurements (CPM)
NISQ Device
NISQ Device
Global-Mode
(50% of Trials)
Subset-Mode
(50% of Trials)
Recompile
Recompile
Bayesian Updates

## Slide 26
Performance Of JigSaw
How does recompilation help? How about combining with other methods?
Average: 3.1x
Best-Case: 8.4x

## Slide 27
Performance Of JigSaw
JigSaw combined with other techniques is even more effective
3.25x higher probability of success
Avg. 2.x Max: 7.8x with recompilation
Can be combined with other methods
EDM: Ensemble of Diverse Mappings [Prior work that used multiple mappings to run a program]

## Slide 28
Improved STATE Classification
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 29
Measurement Output Classification
Qubit readout translates an analog signal into digital information
State-Of-The-Art Classifier Design
ADC
Qubit state classifier
0 to 31
Multiplexed readout
Signal
(5 qubits)
0/1
>½ million parameters!
Qubits
Readout signal
A state-dependent readout signal is acquired from the qubits that is digitized by an Analog-to-Digital Converter.
This digitized data is used for state classification.
ADC
1000 sample buffer
Time
dependent
signal
1Lienhard, Benjamin, et al. "Deep-neural-network discrimination of multiplexed superconducting-qubit states." Physical Review Applied 17.1 (2022): 014024.

## Slide 30
What About Implementation Of The NN Classifier?
Hardware complexity of NN classifiers limit their adoption
0 - 31
Multiplexed readout
Signal
(5 qubits)
>½ million parameters!
ADC
1000 sample buffer
Up to 25% reduction in state assignment error rate compared to contemporary classifiers.
Up to 10x reduction in readout crosstalk.
High hardware complexity (>100% LUT utilization on Xilinx MPSoCs)
But…..
Slow if implemented in software

## Slide 31
Understanding Measurement Classifier Space
Ideally, we want the benefits of NN at lower complexity as IBM’s classifier
Retain crosstalk mitigation advantages offered by neural networks.
Reduce hardware complexity.
Readout Error
Classification latency /
Hardware complexity
IBM hardware classifier
Large FNN Classifier
Hardware classifiers
Software classifiers

## Slide 32
Visualizing Readout Process
ADC
Qubits
Inphase (I)
Quadrature (Q)
The readout signal is split into two channels – Inphase (I) and Quadrature (Q).
The readout signal is received from the qubits is a continuous time signal of duration > 100ns.

## Slide 33
Visualizing Readout Process
ADC
Qubits
Inphase (I)
Quadrature (Q)
The readout signal is split into two channels – Inphase (I) and Quadrature (Q).
The readout signal is received from the qubits is a continuous time signal of duration > 100ns.

## Slide 34
Visualizing Readout Process
ADC
Qubits
I
Q
Filter
Classifier
Filtering reduces the dimension of the input signal – usually an averaging filter.
1000s of shots
The readout signal is split into two channels – Inphase (I) and Quadrature (Q).
The readout signal is received from the qubits is a continuous time signal of duration > 100ns.

## Slide 35
Reality Of Readout Process
Qubits relax to their ground state during the long-latency measurement process
Chart: Per Qubit Misclassifications
| Qubit 1 | Qubit 2 | Qubit 3 | Qubit 4 | Qubit 5
0 | 7.17 | 105.444 | 27.502 | 29.439 | 11.33
1 | 27.987 | 186.059 | 83.024 | 42.673 | 37.165
Qubits prepared in state ‘1’ relax back to the ground state during readout
(Reality)

## Slide 36
Detecting Relaxations
Traces corresponding to relaxations are distinct, can be detected using template matching

## Slide 37
Template Matching
Matched filters enable us to perform template matching and detect qubit relaxations
Input
Template
Match /
No match
Template matching
Matched filter

## Slide 38
Relaxation Matched Filters
The RMFs are designed to detect the qubit relaxations
Readout
Signal
0 - 31
Use traces corresponding to relaxations for
training Relaxation Matched Filters (RMF)
parameters
MF
RMF
0 or 1?
True 0 or 10?
MF
RMF
NN
HERQULES
Satvik Maurya et al. “Scaling Qubit Readout with Hardware Efficient Machine Learning Architectures”, ISCA 2023

## Slide 39
HERQULES Performance Overview
HERQULES enables qubit state classification with greater accuracy
 | Baseline1 | HERQULES
Qubit 1 | 0.969 | 0.985
Qubit 2 | 0.753 | 0.754
Qubit 3 | 0.943 | 0.966
Qubit 4 | 0.946 | 0.962
Qubit 5 | 0.97 | 0.989
Ƒ5Q | 0.9122 | 0.9266
16% relative improvement
Chart: Resource utilization on a Xilinx MPSoC
| LUT | FF | BRAM | DSP
Baseline | 468.64 | 133.96 | 2.56 | 100
HERQULES | 7.79 | 0.75 | 2.56 | 1.85
If an FPGA large enough to fit the baseline is used, HERQULES can fit the hardware required for readout of >10x more qubits.

## Slide 40
What About Latency Of Measurement Operations?
Fast and accurate readout at scale remains an open problem
HERQULES can achieve higher readout accuracy with
a shorter readout duration without requiring re-training.

## Slide 41
Summary
Measurement errors can be reduced at the device-level, by performing measurements in a less vulnerable state, via device characterization followed by output post-processing, and by using enhanced classifier to classify the output states.
Measurement errors depend on the quantum state, we can transform a more vulnerable state into a less error-prone one before measuring.
We can assess the probabilities of incorrectly measuring each state as another via device characterization and use this information to rectify the output distribution. We can use measurement subsets and recompilation to further improve fidelity.
Readout errors happen due to qubits relaxing during these long-latency operations. We can detect them by designing more accurate classifiers to determine output states accurately.
Fast and accurate readouts are desirable, remains an open problem.