## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
ECE 382V: QUANTUM COMPUTING SYSTEMS:
A SOFTWARE/ ARCHITECTURE PERSPECTIVE
Variational Quantum
Algorithms

## Slide 2
Quantum Algorithms For Near-Term Systems
NISQ algorithms promise to demonstrate quantum advantage in the next few years
Exponential Speedup
Speedup by
complexity
reduction
Polynomial Speedup
Speedup via
Heuristic
Shor’s
Factoring
Quantum
Simulation
Grover
Search
Bernstein
Vazirani
Strong guarantees on
quality of solution
Approximate
Optimization
(QAOA)
Chemistry
Simulation
VQE
Weak guarantees on
quality of solution
Requires many gates, qubits, and long coherence times
Can work on NISQ systems, require limited coherence

## Slide 3
Example Application Domain: Combinatorial Optimization
Many real-world problems are combinatorial optimization problems
Traveling Salesman Problem: Given a list of cities and the distances between each pair of cities, what is the shortest possible route that visits each city exactly once and returns to the origin city?
Knapsack Problem: which boxes should be chosen to maximize the amount of money while still keeping the overall weight under or equal to 15 kg?

## Slide 4
Hamiltonian And Energy
Can we find the ground state?
The Hamiltonian is an operator that represents the total energy of a quantum system
The Energy of a quantum system in state|𝜓⟩ is given by the expectation value E(|𝜓⟩)
The ground state of a system (|𝜓*⟩) is the state with lowest energy (expectation value)

## Slide 5
Trial-And-Error Approach/ Variational Method
The variational method can estimate the ground state of a quantum system or Hamiltonian
U(θ)
qn
n
|𝜓(⟩
Prep trial state or ansatz
Run
Compute E(θ)
Compute Expectation Value
Update 𝜃
Variational Loop

## Slide 6
Combination Optimization Using Variational Methods
Optimizing a cost function mapped onto finding the ground state energy of a Hamiltonian
Combinational
Optimization
Cost function
Ground state energy estimation
Hamiltonian
|𝜓(⟩
Find for which the cost function has minimum/maximum value
Find for which the energy is minimum

## Slide 7
Max-Cut Problems
The 0s and 1s in the solution string corresponds to the two sets
Partition all nodes of given input graph into two set of nodes: Set-0 and Set-1 such that the partition maximizes the number of edges connecting Set-0 nodes to Set-1 nodes
0
4
1
2
3
Input Graph
Example Cut: {0,1,2} and {3,4}
Set-0 Nodes | Set-1 Nodes | Edges cut | Solution String
0, 1, 2 | 3, 4 | E23 and E24 | 11000
1, 2, 3 | 0, 4 | E01 E02 E23 and E24 | 10001
0, 1, 3, 4 | 2 | E12 E02 E23 and E24 | 00100

## Slide 8
Other Examples Of Max-Cut Problems
Max-cut is a combinatorial optimization problem that can be solved using variational method
1
0
2
1
0
Optimal Cut: {0} and {1}
Optimal Cut: {0,2} and {1}
1
0
2
3
Optimal Cut: {1,3} and {2,0}

## Slide 9
QAOA
Quantum Approximate Optimization Algorithm (QAOA)- building circuits, performance of QAOA

## Slide 10
Quantum Approximate Optimization Algorithm (QAOA)
The problem solution is determined from the output distribution of the optimal circuit
For running QAOA on N node input graph G =(V,E), we need N physical qubits
Nodes of graph (V) are mapped on N physical qubits
Problem cost function is represented by coupling qubits corresponding to E
Real-world problem graph
3 nodes
3 qubits
Edges correspond to parametric CPHASE gates

## Slide 11
Parameters Of QAOA Circuits
Higher values of ‘p’ provide greater approximation guarantees
Problem graph
QAOA circuit
The circuit comprises of two parameters ()
Find optimal
Repeat for p layers to create a QAOA circuit with 2p parameters, increasing complexity with p

## Slide 12
Few Key Takeaways From QAOA Circuit Design
How does QAOA perform on actual systems?
The number of CNOT gates in QAOA circuit depends on the number of edges in input graph
The number of measurement operations scale with the number of nodes in the input graph
The actual number of CNOT gates are much larger due to routing overheads
Chart: QAOA Program Size (# Qubits)
| 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Original | 12 | 20 | 30 | 42 | 56 | 72 | 90 | 110 | 132 | 156 | 182 | 210 | 240 | 272 | 306
Sycamore | 18 | 29 | 48 | 69 | 98 | 126 | 165 | 200 | 252 | 267 | 347 | 405 | 474 | 542 | 651
Toronto | 21 | 41 | 54 | 87 | 119 | 150 | 204 | 242 | 339 | 390 | 464 | 561 | 711 | 758 | 951
2x
3x

## Slide 13
QAOA On Real Quantum Hardware
How does QAOA perform on Google Sycamore?
Hardware grid
3-Regular
SK Model
Google studied the performance of QAOA circuits on their Sycamore device
Three types of graphs were chosen: hardware grid, 3-regular, fully-connected (SK model)
The size of the input graph is increased and the performance is observed
No routing overheads
Theoretical guarantees on quality of solution
Stress-test, maximum routing overheads

## Slide 14
Performance Of QAOA On Google Sycamore
What about QAOA performance with increasing layers (p)?
n=23
n=14
n=11

## Slide 15
QAOA Performance With Increasing ‘p’ On Sycamore
Improving the performance of QAOA is an open problem
On real systems, increasing ‘p’ deteriorates performance
Increasing ’p’ leads to more gates making the QAOA circuits more vulnerable to errors
Google Quantum AI “Quantum Approximate Optimization of Non-Planar Graph Problems on a Planar Superconducting Processor”, 2021
Vanishing gradients/ Barren Plateaus

## Slide 16
VQE and QML
Variational Quantum Eigensolver (VQE) and Quantum Machine Learning (QML)

## Slide 17
Variational Quantum Eigensolver (VQE)
Example: The Cr2 molecule, which is often considered a benchmark for quantum advantage in molecular chemistry minimally requires around 50 qubits and has nearly 50,000 Pauli terms
Used the determine the ground state energy of molecules- enable us to determine chemical reaction rates and understand molecular geometries
Estimating the global optimum with high accuracy is crucial
The Hamiltonian is a linear combination of several Pauli terms (they are obtained by measuring the ansatz in different bases)
ZZZ
XZX
The number of terms grow O(N4)

## Slide 18
Quantum Machine Learning (QML)
Designing efficient QML circuits is an open problem
Variational circuits to perform ML tasks
Data embedding to encode classical information using quantum gates
Gradients computed using parameter shift of the VQA parameters (expensive)
Circuits must offer high performance (learning ability) and high noise-resilience

## Slide 19
How Do We Measure VQA Performance?
We must reduce execution time and impact of noise to improve VQA performance
Execution Time
Quality Of Solutions
Cloud latencies
Training steps
Optimization Routine
# Operations
Transient Faults
No gradients
Waiting too long reduces performance of software error mitigation
Lack of gradients hurt the training process, increasing number of iterations

## Slide 20
Approaches For Improving VQA Performance: Overview
VQA performance improvement requires a full-stack approach
Hardware efficient ansatz-> theoretical guarantees?
Instruction re-ordering for enhanced scheduling
Low-overhead application-specific circuit cutting
Reducing impact of transient errors on training performance
Improving the performance of the variational loop
Improving the performance of the optimizer
Reducing total number of iterations in the variational loop

## Slide 21
REDUCE IMPACT OF OPERATIONAL ERRORS*
How can we improve scheduling or circuit cutting by leveraging application-specific properties? Goal is to run fewer operations, more compact circuits, reduce overheads of circuit cutting

## Slide 22
QAOA Specific Instruction Re-ordering
Optimize for higher concurrency by re-ordering operations and gate cancellations
Problem graph
QAOA circuit
Order the CPHASE blocks such that we maximize concurrency
Introduce SWAPs such that CNOTs from the CPHASE and SWAPs cancel
Mahabubul Alam et al. “Circuit Compilation Methodologies for Quantum Approximate Optimization Algorithm”, MICRO 2020

## Slide 23
QAOA Specific Low Overhead Circuit Cutting
Hotspots contribute maximum number of operations and SWAP overheads in QAOA
Real-world problem graphs tend to have hotspots
Freeze the hotspots
Ramin Ayanzadeh et al. “FrozenQubits: Boosting Fidelity of QAOA by Skipping Hotspot Nodes”, ASPLOS 2023

## Slide 24
REDUCE IMPACT OF TRANSIENT FAULTS
By reducing cloud latencies and number of training steps

## Slide 25
What Are Transient Faults?
Transient faults are hard to fully eliminate at the device-level
T1 (us)
10
20
60
25
100
75
50
Potential transient errors!
30 40 50
Time (hours)
T1 relaxation: loss of energy of qubit from excited state
|1> to the ground state |0>
Fabrication defects
Parasitic coupling
Two level systems
Thermal ﬂuctuations
Quasi particles
Burnett et al. “Decoherence benchmarking of superconducting qubits” NPJ Quantum 2019

## Slide 26
Transient Faults Impact Variational Loop Performance
Transient faults may lead to traversal along incorrect paths on the optimization landscape
Transient effects
100th ->500th iteration benefit effectively nil

## Slide 27
How Do We Eliminate Transient Faults In VQAs?
By comparing the gradients from both iterations, impact of transient faults can be reduced
ith
VQA Circuit(s)
(i+1)th VQA Circuit(s)
(i+2)th VQA Circuit(s)
(i+2)th VQA Circuit(s)
ith
VQA Circuit(s)
(i+1)th VQA Circuit(s)
(i+1)th VQA Circuit(s)
ith
VQA Circuit(s)
(i+1)th VQA Circuit(s)
(i+1)th VQA Circuit(s)
(i+2)th VQA Circuit(s)
Gokul Ravi et al. “Navigating the dynamic noise landscape of variational quantum algorithms with QISMET”, ASPLOS 2023

## Slide 28
Performance Of QISMET
QISMET efficiently mitigates a large portion of the transient noise impact on VQAs and is able to improve the fidelity by 1.3x-3x over a traditional VQA baseline,
6-qubit TFIM VQA on IBMQ Sydney run over a 48-hour period
6-qubit TFIM VQA on IBMQ Guadalupe run over a 48-hour period

## Slide 29
REDUCE RUNTIME OF Variational Loop
By reducing cloud latencies, improving classical optimizer performance, and reducing the number of training steps in the variational step

## Slide 30
Qiskit Runtime: Improving Variational Loop Performance
What do we need from services such as Qiskit Runtime?
+
+
+
+
+
+
+
+
Optimizer
Optimizer
Long cloud latency bottlenecks performance of variational quantum algorithms such as QAOA
Containerized environment

## Slide 31
QAOA Performance Depends On Optimizer Performance
Poor optimizers may not find the optimal solution and/or takes too long to converge
Some optimizers can deal with noisy data more efficiently than others
Energy convergence for a problem
Optimizers like SPSA preferred
Models to improve optimizers for QAOA
Kevin Sung et al. “Using models to improve optimizers for variational quantum algorithms”, https://iopscience.iop.org/article/10.1088/2058-9565/abb6d9/ampdf

## Slide 32
Minimizing Overheads Of VQE Using Clifford Circuits
How can we use the Clifford space to reduce VQE training overheads?
Noise induced local minimum
NOISE FREE!!
Portion of the quantum space can be simulated on classical systems efficiently(Clifford space)

## Slide 33
The Clifford circuits enable us to start the search from parameters close to the global optimum
Find The Best Parameters In The Clifford Space
=
Bayesian Optimization
Tuning Parameter

## Slide 34
Clifford And Non-Clifford Space
For more details on how the Clifford circuits are trained, read the “CAFQA” paper
Parameterized ansatz circuit
A classically simulable Clifford circuit
Discrete angles = {0, pi/2, pi, 3*pi/2}
A classically intractable general circuit
Continuous angles = [0, 2*pi]
Clifford + Non-Clifford Space
Clifford Space
Gokul Ravi et al. “CAFQA: A classical simulation bootstrap for variational quantum algorithms”, ASPLOS 2023

## Slide 35
Performance Of CAFQA
CAFQA achieves similar accuracy with fewer iterations
CAFQA: 100x higher
initial accuracy
CAFQA: 80 itns to converge
HF: ~1000 itns to converge (12x worse)
HF: 3x worse error
Objective
Hartree-Fock initialization [~1930]: Classically-solvable algorithm in molecular chemistry that approximates
/ restricts the problem’s electronic configuration.

## Slide 36
Key Takeaways From Variational Quantum Algorithms
Development of NISQ applications is an active area of research
Limited applicability
Limited speedup
Performance limited by the high error-rates of the quantum hardware
Demonstration of computational advantage using VQAs (such as QAOA) requires us to solve problems involving hundreds of qubits and thousands of quantum operations
Will VQAs offer practical quantum advantage? What does this mean for the quantum field?