## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
ECE 382V: QUANTUM COMPUTING SYSTEMS:
A SOFTWARE/ ARCHITECTURE PERSPECTIVE
QUANTUM ERROR CORRECTIOn

## Slide 2
Applications To Devices Gap
Most practical quantum applications require error-rates far below device error-rates
2023
2026
203X
~400 qubits
p = 0.5%
~4000 qubits
p = 0.1%
~100K qubits
p = 0.01%
Goal
Applications-at-scale
p < 10-15
Significant gap in error rates!

## Slide 3
Triple Modular Redundancy (TMR)
What happens if double-bit failures happen?
Classical bit
Replicate 3 times: 0 as 000, 1 as 111
1
1
1
Copy
Triple Modular Redundancy
Majority
Measure
0
Tolerate single-bit errors

## Slide 4
Triple Modular Redundancy (TMR)
TMR can only tolerate single-bit errors
Replicate 3 times: 0 as 000, 1 as 111
1
1
1
Copy
Triple Modular Redundancy
Majority
Measure
0
Tolerate single-bit errors
0
Cannot tolerate double-bit errors
Classical bit

## Slide 5
Errors Represented As Code-Words
Correctable/uncorrectable errors fall into groups of valid/Invalid code-words in Hamming space
Single-bit Errors
Double-bit Errors

## Slide 6
Increased Redundancy For Greater Fault-Tolerance
TMR can correct a single bit failure, 5MR can correct two bit failures
0
1
1
Copy
Triple Modular Redundancy
Majority
Measure
0
Tolerate single-bit errors
1
1
Replicate 5 times: 0 as 00000, 1 as 11111
Majority
5MR
Tolerate double-bit errors
Classical bit

## Slide 7
Code Distance
How does this look for 5MR?
000
HD-0
001,010,100
HD-1
011,110,101
HD-2
111
HD-3

## Slide 8
Code Distance
A code of distance d corrects up to (d-1)/2 errors
00000
HD-0
00001…
HD-1
01111…
HD-4
11111
HD-5
00011…
HD-2
00011…
HD-3

## Slide 9
Quantum Error Correction
QEC needs an approach different from classical techniques
Quantum error correction is fundamentally different from classical methods
1
1
1
Classical bit
Copy
Triple Modular Redundancy
Majority
Measure
0
Tolerate single-bit errors
Quantum bit
Copy
Measure

## Slide 10
Repetition Code
This repetition code can correct bit-flip errors
1
0
0
1
q[0]
q[1]
q[2]
0
0
None
1
0
q[0]
1
1
q[1]
0
1
q[2]

## Slide 11
Shor 9-bit Code
High redundancy, computation is hard using Shor’s code [X,Z are easy]

## Slide 12
Steane 7-bit Code
Lower redundancy than Shor’ code, computation of T is still hard [X, Z, CNOT, and H are easy]

## Slide 13
Recursion For Greater Fault Protection?
Greater redundancy for greater fault protection
b
b
b
b
b
b
b
b
b
b
b
b
b
TMR
TMR-of-TMR
b
b
b
What is the minimum number of errors that can cause the TMR-of-TMR to fail?
Concatenation code: Take a qubit and encode it in the 7-qubit Steane code.
Take each physical qubit that is part of the logical qubit & RE-ENCODE in 7-qubit code

## Slide 14
Steane 49-bit Code
Steane 49-bit code can correct up to 4 errors

## Slide 15
Quantum Error Correction: Overview
Errors are detected by using syndrome extraction and decoding the syndromes
QEC involves syndrome (parity) extraction and decoding to identify errors
Decoder
Control
Processor
Qubits
Readout
Interface
Syndrome
01…….01
Correction
QEC
Instructions
Did an error occur?
Where did the error occur?
What was the type of error?
1
1
Instructions to generate syndrome
2
2
Send syndrome to decoder
3
3
Send correction to control processor

## Slide 16
Quantum Error Correction: Unique Challenges
Significant amount of research effort in QEC
Huge redundancy
Must be very fast
Imperfect process
System-level challenges
High overheads
(operations, qubits)
Operations at scale
Low coherence
Errors quickly accumulate
Both instruction delivery and decoding
Incorrect parities
Complex errors
(correlated, leakage)
Bandwidth
Cryogenic
Latency
Low overhead codes
Faster decoders (approx. algo., hardware)
Handling via decoding, scheduling
uarchitecture, compression, multi-level design

## Slide 17
Quantum Error Correction Codes: Performance Metrics
Which QEC code is the best depends on many factors. Surface codes widely considered most promising due to its grid structure, polynomial time decoding algorithm, and high threshold.
Redundancy (lower is better), structure
Decoder (easy to decode*)
Hardness of operations
Threshold
Steane code over Shor code
QLDPC codes over surface codes
Surface codes over Color codes
Surface codes over QLDPC codes
Steane code over Shor code
*Depends on decoding strategy
Plogical < Pphysical only if
Pphysical < Pthreshold
Surface codes(grid) over QLDPC codes
Surface codes over Color codes

## Slide 18
QEC @ Scale: Need System-Level Thinking
How do we design the control processors? How do we transmit information?
Decoder
Control
Processor
Large Distances, 100s-1000s of Logical Qubits
Readout
Interface
Correction
QEC
Instructions
Syndrome
15-20 mK
(Inside dilution refrigerator)
Room temperature
(Outside dilution refrigerator)
4 K
(Inside dilution refrigerator)
4 K
Existing decoders do not account for the system-level constraints
Large bandwidth
More noise
Number of wires
100s Gbps
Inefficient

## Slide 19
Rest Of QEC Discussion: Overview
Surface codes and decoding surface codes
Approximate decoding techniques for surface codes
Bandwidth challenges in QEC [both control and decoding]
QEC demonstrations and focus on eliminating certain types of errors [leakage]
Mapping surface codes to non-grid lattices [Grid surface code on IBM’s heavy-hex lattice]
QLDPC codes [Guest lecture by Nicolas Delfosse from Microsoft]