## Slide 1
POULAMI DAS
ECE, The University of Texas at Austin
ECE 382V: QUANTUM COMPUTING SYSTEMS:
A SOFTWARE/ ARCHITECTURE PERSPECTIVE
CROSSTALK & IDLE error mitigATION

## Slide 2
What Is Crosstalk In Quantum Systems?
Operation on one device impacts the error-rate of an operation on another due to crosstalk
Isolated
Multiple
The effective measurement error-rate of a qubit increases in the presence of other measurements due to readout crosstalk.
The effective error-rate of a two-qubit CNOT gate increases in the presence of other CNOTs due to operational crosstalk.
Isolated
Multiple

## Slide 3
CNOT-CNOT Crosstalk
Trade-off between serial CNOT scheduling and increased probability of decohering
+
+
+
H
q0
q1
q2
q3
Parallel CNOTs
for depth reduction
Crosstalk
+
+
+
H
q0
q1
q2
q3
Serial CNOTs
for crosstalk reduction
Decoherence

## Slide 4
Reduce Both CNOT-CNOT Crosstalk And Decoherence
Not all CNOT pairs are equally susceptible to crosstalk, schedule low crosstalk pairs in parallel
Ideally, we want to reduce both crosstalk (via serial CNOT scheduling) and the probability of decoherence (by maximizing parallel CNOT scheduling)
Not all pairs of CNOTs are impacted by crosstalk errors equally
Low
High
Too High

## Slide 5
CNOT-CNOT Crosstalk Reduction Via Scheduling
+
+
+
H
q0
q1
q2
q3
+
+
+
q4
q5
q6
+
+
+
+
H
q0
q1
q2
q3
+
+
+
q4
q5
q6
+
High crosstalk CNOT pair scheduled serially
How do we determine which pairs of CNOTs are high crosstalk pairs?
Parallel CNOTs reduce
decoherence
Serial CNOTs reduce
crosstalk
High crosstalk

## Slide 6
Identifying High-Crosstalk CNOT Pairs
The information from the device characterization is used by the compiler during scheduling
Characterize
Determine CNOT error-rates in isolation
Determine the CNOT error-rates for simultaneous CNOTs
Compare

## Slide 7
Compilation Workflow To Reduce CNOT-CNOT Crosstalk
What are the drawbacks of this approach?
Characterize
Database
n-bit
Program
Compiler
(Schedule Pass)
Executable
If two CNOTs can be scheduled in parallel because they do not have any dependencies and the CNOT pair is not a part of the high crosstalk database, then they are scheduled concurrently

## Slide 8
Characterization Complexity Scales Exponentially
Localized characterization incurs reduced overheads
Crosstalk tends to be local, characterize spatial neighbors
The number of CNOT pairs that must be characterized grows exponentially with the system size
Prakash Murali et al. “Software Mitigation of Crosstalk”

## Slide 9
IDLE Error Mitigation
Why quantum computing? What topics will be covered? What are the requirements and expected outcomes?

## Slide 10
Qubit Encounter Errors Even When Idle
Crosstalk from on-going operations significantly increase idle errors
Qubits encounter errors while performing operations: Active Errors
Error!
Error!
Decoherence
Crosstalk increases idling errors by 10x
Qubits are vulnerable to errors even while they are not performing operations: Idling Errors
Time = 0
Time = t (100 µS)
1
0
1
0

## Slide 11
Idle Errors At Program-Level
Idle qubits are common in quantum programs
Long-latency of two-qubit operations
Data-dependencies
35ns
idle
2400 ns
Chart: Bernstein Vazirani Circuit Size
| 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 2.4178 | 4.4302 | 6.3289 | 8.1707 | 10.3822 | 12.3947 | 14.2791 | 16.5191 | 18.2044 | 19.9253 | 21.7031 | 23.3529 | 25.0738 | 26.9227 | 28.8007 | 29.9804 | 31.4311
SWAP
operations

## Slide 12
How Do We Reduce Idle Times On Qubits?
What are the drawbacks of this scheme?
+
X
q0
q1
q2
+
+
t=0
t=40
t=440
t=800
t=840
By default, operations are scheduled as late as possible (ALAP) to minimize decoherence
X
t=1240
X-gate: 40 ns
CNOT gate: 400 ns
ALAP policy schedules X when 40 ns are left for the CNOT to complete
Idle:
360
Schedule available (single) gates at the middle of idle time windows
t=620
Idle:
180
Idle:
180
Kaitlin Smith et al. “TimeStitch: Exploiting Slack to Mitigate Decoherence in Quantum Circuits”

## Slide 13
Dynamical Decoupling
Dynamical decoupling keeps idle qubits busy without altering their state
Dynamical Decoupling (DD): Keep idle qubits busy
Specific gate sequence: X-X or X-Y-X-Y
Effectively Identity gate: Qubit state remains unchanged

## Slide 14
Is Dynamical Decoupling Always Helpful?
How do we identify which qubits to apply DD pulses to for maximum success-rate improvement?
No-DD
DD-for-All
Best Sequence: 010100
DD
DD
DD
DD
DD
DD

## Slide 15
Knowing Which Qubits Will Benefit From DD Is Hard
How do we identify the subset of qubits that will likely benefit the most from DD?
Challenge-1: Which qubits will benefit from DD? Hard to characterize all possibilities
0
1
Challenge-2: Do not know correct output.
Thus, can't test fidelity with DD sequences
DD
DD
2
3
4
5
Don’t know
which is better

## Slide 16
Use Decoy Circuits To Learn
Drawback: the search scales exponentially
Clifford circuits an be simulated
efficiently to find noiseless output
Crosstalk from CNOTs is the dominant source of idling errors
Poulami Das et al. “ADAPT: Adaptive Dynamical Decoupling”, MICRO 2021

## Slide 17
Use Local Search
The local search makes this approach scalable
210 = 1024
Decoy Circuits
Not Scalable
DD
DD
DD
DD
DD
...
16 Decoy Circuits
DD
DD
DD
DD
DD
...
Best: 0101
16 Decoy Circuits
Best: 1101
DD
DD
DD
...
4 Decoy Circuits
Best: 01
Total Decoy Circuits: 36
Optimal Sequence: 0101110101

## Slide 18
ADAPT: Performance Overview
ADAPT is effective in reducing idling errors
ADAPT is effective: 1.6x on average (including other machines)
Optimal DD sequence from ADAPT outperforms DD-on-All Qubits
Chart: Benchmarks on IBMQ-Toronto (With XX DD Sequence)
| QPEA-5 | BV-7 | QFT-6 | BV-8 | Gmean
All-DD | 1.0102 | 1.1656 | 1.6 | 1.1983 | 1.392
ADAPT | 1.2317 | 1.2409 | 1.8 | 1.4324 | 1.5975
Runtime Best | 1.2317 | 1.3977 | 2 | 1.4324 | 1.789
2.3
2.7
3.3

## Slide 19
Summary
Idle errors are common in quantum circuits.
Idle errors worsen in the presence of crosstalk from on-going CNOT operations.
Idle errors can be reduced by keeping qubits busy (dynamical decoupling).
Crosstalk and idle errors depend on the basis gate set and device characteristics (IBM vs. Google devices have different crosstalk behavior).
Translating device-level approaches to program-level is non-trivial, we must rethink.
Studying crosstalk and idle errors in the context of QEC is an important open problem